## Slide 1
TEAM 03
Motion Controlled Lamp
Ian Tarleton
Kainoa Kekahuna
Grant Cazinha
James Schiffer
12/08/2015
ECE 411

## Slide 2
Problem/Need
Create a low cost lamp that requires no physical contact to turn on/off, or to adjust the level of illumination.

## Slide 3
Motivation
We thought this would be a cool novelty device. It could be a fabulous gift, and even a conversation piece in the home.

## Slide 4
Objective
Complete a new product introduction using the processes and methods introduced in ECE 411 with the ultimate goal of creating a working prototype of our touch-free lamp

## Slide 5
Alternatives
Based on our research, there is nothing that functions like the lamp that we designed and constructed.

## Slide 6
Requirements
Lamp Features
Approximately 40W incandescent equivalent (300 Lumens) illumination.
The device will be turned on and off using motion detection.
  Accuracy within 12" beyond the minimum distance for the sensor.
Illumination variability control based on distance from sensor.
  Adjustable based on distance measurements in a 12" range starting from the minimum distance of the sensor.
    Decreasing distance decreases illumination down to 0% of maximum.
    Increasing distance increases illumination up to 100% of maximum.
Uses standard 120V outlet for power.
Cost
Cost for a single prototype will be less than $100.
Operational Environment
Standard Residential usage.
Manufacturing
PCB
  Have ≥ 2 layers, with solder mask and at least a top-side silk screen.
  Have an area between > 9 cm2 and < 900 cm2.
  Have no linear dimension < 2 cm or > 30 cm.

## Slide 7
Approach
  We implemented the Waterfall design process
  This matched well with course requirements
  Better for hardware based projects (compared to SCRUM, AGILE, etc.)

## Slide 8
Schedule
  Full Schedule available on our Github repo:
  https://github.com/j1mb0/ECE411/tree/master/T03_Schedule

## Slide 9
Motion
Controlled
Lamp
Light
Emission 300 Lumens
Motion
Sensor
Power
12 Volts DC
Module | Motion Controlled Lamp
Inputs | Motion: Object distance, range 2”-14” 12 V DC
Outputs | Light (300 Lumens)
Functionality | Converts proximity based motion controls into light emission
Level 0 Block Diagram

## Slide 10
User
Micro Controller
LED Array
Hand
Ultrasonic Range Finder
CCCS
PWM Signal
Physical View (UML)
Distance
(2”-14” from sensor)
Processor Continuously
Sampling and Averaging 2 samples every 4 ms

## Slide 11: Design - Hardware Considerations
Sensor
  IR
    Susceptible to interference
    Unsure of interface with hand due to body heat at close distances
  Ultrasonic
    Less susceptible to interference
    Functions within distance specified in requirements
Illumination
  LEDs
    Low cost
    Low power requirements
    Long life span
    Low heat dissipation
Power
  5V Micro USB (standard phone charging cable and wall wart)
    Not enough voltage
  12V Wall Wart
    Delivers enough voltage

## Slide 12
Design - Hardware
PCB
  Have ≥ 2 layers, with solder mask and at least a top-side silk screen.
  Have an area between > 9 cm2 and < 900 cm2.
  Have no linear dimension < 2 cm or > 30 cm.
Sensor
  Ultrasonic Range Finder
Illumination
  Array of 1W LEDs
Power
  12V Wall Wart

## Slide 13: Design - Software
Used Atmel Studio
Code Written in AVR Baremetal C
Used AVR Dude to load software onto ATMega328-MU

## Slide 14: Implementation – Major Components
ATMega328-MU
L7805 Voltage Regulator
DMN3024LSD NFET
ZDT694 NPN Transistor
1W LED
HC-SR04 Ultrasonic Range Finder
12V Wall Wart
LED Heat Sink

## Slide 15: Constant Current Source

## Slide 16: Implementation - Schematic

## Slide 17: Implementation - Board

## Slide 18: Implementation - Tools Employed
EagleCAD
Atmel Studio
AVR Dude
Microsoft Project

## Slide 19: IP and Prior Work
PWM code concept from Arduino website
High Power LED Driver Circuit Design from Dan Goldwater – Cofounder of Instructables.com
Base schematic design was structured around the Arduino Tiny schematic
We did not knowingly use any IP from external sources

## Slide 20: Testing – Test Plan
System Tests
  Software:
    Test Input data. Send test data equivalent to the sensor data. Confirm that data was received and compare with test input data.
    Test sensor input data conversion. Send input test data. Allow conversion to pulse width modulation values. Compare with expected pulse width modulation values.
    Test output data. Send output data. Was output data sent and was that data equivalent to the data given.
  Hardware:
    Test 12V wall wart to ensure the 12V DC is the proper output.
    Test voltage regulator from 12V DC to 5V DC with oscilloscope.
    Test ultrasonic range module input and output signals using function generator and oscilloscope.
    Test processor inputs and outputs using oscilloscope and function generator.
    Test Led array range of illumination using power supply.

## Slide 21: Testing – Detailed Test Descriptions
Test Writer: |  | Grant Cazinha |  |  |  |  | 
Test Case Name: |  | LED Array Illumination Test |  |  |  | Test ID #: | MCL-LA-01
Description: |  | Test Led array range of illumination using power supply increasing current from 0 to 100% of max current rating for LEDs in 10 steps. This is a measure of the brightness level of the LEDs. |  |  |  | Type: | White Box
Tester Information |  |  |  |  |  |  | 
Name of Tester: |  | James Schiffer |  |  |  | Date: | 11/15/2015
Hardware Ver: |  | 2.0 |  |  |  | Time: | 6:17 PM
Setup: |  | Attach power supply leads to LED board. |  |  |  |  | 
Step | Action | Expected Result | Pass | Fail | N/A | Comments | 
1 | 10% | 35mA | x |  |  | +- 1mA | 
2 | 20% | 70mA | x |  |  | +- 1mA | 
3 | 30% | 105mA | x |  |  | +- 1mA | 
4 | 40% | 140mA | x |  |  | +- 1mA | 
5 | 50% | 175mA | x |  |  | +- 1mA | 
6 | 60% | 210mA | x |  |  | +- 1mA | 
7 | 70% | 245mA | x |  |  | +- 1mA | 
8 | 80% | 270mA | x |  |  | +- 1mA | 
9 | 90% | 315mA | x |  |  | +- 1mA | 
10 | 100% | 350mA | x |  |  | +- 1mA | 
Overall test result: |  |  | x |  |  | Well within range of expected current | 

## Slide 22: Testing – Detailed Test Descriptions
Test Writer: |  | Grant Cazinha |  |  |  |  | 
Test Case Name: |  | 12V Wall Wart Voltage Verification |  |  |  | Test ID #: | MCL-WW-01
Description: |  | Test 12V wall wart to ensure the 12V DC is the proper output. |  |  |  | Type: | Black Box
Tester Information |  |  |  |  |  |  | 
Name of Tester: |  | James Schiffer / Kainoa Kekahuna |  |  |  | Date: | 11/30/2015
Hardware Ver: |  | 2.0 |  |  |  | Time: | 3:00 PM
Setup: |  | Wall wart plugged into board and wall electrical socket |  |  |  |  | 
Step | Action | Expected Result | Pass | Fail | N/A | Comments | 
1 | Plug wall wart into wall electrical socket | N/A |  |  | x |  | 
2 | Plug wall wart into board | N/A |  |  | x |  | 
3 | Check voltage using oscilloscope | 12V +- 30% | x |  |  | 11.9V- 12.2V Fluctuating. Well within tolerance. | 
Overall test result: |  |  | x |  |  |  | 

## Slide 23: Testing – Detailed Test Descriptions
Test Writer: |  | Kainoa Kekahuna |  |  |  |  | 
Test Case Name: |  | Voltage Regulation Verification |  |  |  | Test ID #: | MCL-VR-01
Description: |  | Test voltage regulator from 12V DC to 5V DC with oscilloscope. |  |  |  | Type: | White Box
Tester Information |  |  |  |  |  |  | 
Name of Tester: |  | James Schiffer, Ian Tarleton |  |  |  | Date: | 11/30/2015
Hardware Ver: |  | 2.0 |  |  |  | Time: | 3:15 PM
Setup: |  | Plug wall wart into eletrical wall socket and plug voltage regulator into board |  |  |  |  | 
Step | Action | Expected Result | Pass | Fail | N/A | Comments | 
1 | Turn on board | n/a |  |  | x |  | 
2 | Test output of voltage regulator with oscilloscope | 5V output from voltage regulator | x |  |  | Oscilloscope read ~5.017V on voltage regulator output | 
Overall test result: |  |  | x |  |  |  | 

## Slide 24: Testing – Detailed Test Descriptions
Test Writer: |  | Grant Cazinha |  |  |  |  | 
Test Case Name: |  | Input Signal to Pulse Width Modulation Conversion |  |  |  | Test ID #: | MCL-PWM-01
Description: |  | Test sensor input data conversion. Send input test data. Allow conversion to pulse width modulation values. Compare with expected pulse width modulation values. |  |  |  | Type: | White Box
Tester Information |  |  |  |  |  |  | 
Name of Tester: |  | James Schiffer, Kainoa Kekahuna |  |  |  | Date: | 11/30/2015
Hardware Ver: |  | 2.0 |  |  |  | Time: | 4:00 PM
Setup: |  | PWM code is configured to set the PWM signal to high after 16 microseconds once loaded onto the board. Connect TinyUSB AVR to board and load code from Atmel Studio. |  |  |  |  | 
Step | Action | Expected Result | Pass | Fail | N/A | Comments | 
1 | Setup Oscilloscope to Read PWM Line | n/a |  |  | x |  | 
2 | Run test by loading PWM code into board | n/a |  |  | x |  | 
3 | Compare output data with expected | PWM signal set to high after 16 microseconds | x |  |  | AVR fuses are factory set to divide run with an internal clock of 1 MHz.. Oscillator was acting with a 1 MHz pulse instead of expected 16MHz pulse. Fixed. | 
Overall test result: |  |  | x |  |  | Successful after adjusting fuse bits. | 

## Slide 25: Results
Did Not Work
  Initial design included LED driver chip. Chip was either faulty or implementation was poor.
  Ordering parts was complicated. We received a few parts that were not what was desired.
  Original power supply concept was not sufficient for the types of LEDs chosen for the lamp.
Worked
  Constant current source design using NFETs was simple and elegant and worked sufficiently.
  Solder stencil and oven for soldering the surface mount components.
  The Lamp

## Slide 26: Contributions
Ian Tarleton
  Designed and Constructed Enclosure
  Documentation
  Quality Assurance / Review
  Component Research
  Debugging
Grant Cazinha
  PCB Design
  Board Construction and Troubleshooting
  Component Research
  Documentation
  Quality Assurance / Review
Kainoa Kekahuna
  Scheduling
  Documentation
  Component Research
  Quality Assurance / Review
  Debugging
James Schiffer
  PCB Design
  Schematic Design
  Component Research
  Debugging
  Coding
  Quality Assurance / Review

## Slide 27: Bill of Materials
Bill of Materials To Construct One Motion Controlled Lamp |  | 
Quantity | Part List | Cost
2 | 10uF Capacitor | $0.30
5 | 0.1uF Capacitor | $0.06
2 | 22pF Capacitor | $0.06
1 | 100k Resistor | $0.32
1 | 10k Resistor | $0.15
1 | 1.5 Resistor | $0.92
1 | ATMEGA328P-MU Processor | $3.38
1 | L7805 Voltage Regulator | $0.62
1 | 16 MHz Crystal Oscillator | $0.79
1 | DMN3024LSD NFET | $0.63
1 | ZDT694CT NPN | $1.16
1 | 12V Wall Wart | $8.93
1 | PCB Manufacturing | $5.00
6 | 1W LED | $1.20
1 | LED Heat Sink | $7.59
1 | Transistor Heat Sink | $0.50
1 | HC-SR04 Ultrasonic Range Finder | $2.47
1 | Power Connection | $1.00
5 | Headers | $0.60
1 | Acrylic With Custom Cuts | $12.00
 | Total Cost of Raw Materials | $47.68
One Time Purchases / Bulk Purchases |  | 
1 | Acrylic Cement | $5.00
1 | Waterproof Sealant | $4.00
1 | TinyUSB (Necessary to Program Board) | $15.00
 | Total Cost With One Time Purchases | $71.68

## Slide 28: Repository
  Full documentation, code, design process, research, etc. available at https://github.com/j1mb0/ECE411/wiki

## Slide 29: Lessons Learned